Evaluation of Collisional-Radiative Model for Argon I on the Texas Helimak
Qualifier Seminar by
K. Carter Dodd
Adviser: Kenneth Gentle, William Rowan

---
Goals
Understand and test structure of a collisional-radiative model for Ar I.
Compare predictions of model using the Texas Helimak.

---
Emission Spectroscopy
Passively gain information on state of plasmas
  - Plasma constituents, impurities, ionization states
  - Density
  - Temperature
  - Bulk motion

---
Atomic States as Populations
Each state is independent population.
Spectral line intensity proportional to population density.

---
Simple Models for Populations
High Density
Collisional Transitions Dominate (detailed balance)
Thermal Equilibrium
Low Density
Radiative Transitions Dominate (“coronal” limit)

---
Collisional-Radiative Model
Medium Density: develop full rate equations.
Can include many different rate processes.
Solve system of equations for level population, which then gives line emission.
In principle, could be “inverted” for density, temperature, ...

---
Collisional Processes
Electron and atomic impact excitation, de-excitation, ionization, and three-body recombination
Assume isotropic Maxwellian distribution.
Example semi-empirical cross-section:

---
Radiative Processes
Photo-excitation, photo-ionization, radiative decay, and radiative recombination.
  - Spontaneous emissions:
  - Photo-excitation accounted for by escape factor:
  - Optically thick:
  - Optically thin.

---
Argon Level Model
Complex level structure.
Levels of similar energy are grouped together to simplify model. Is this valid?
Can higher levels be removed? Compare results to models which do not include them.
Level population solution depends on plasma parameters: neutral density, ion density, and electron temperature and density.
[2]

---
Level 11 Populating

---
Level 7 Populating

---
Removing Higher Levels
(makes a difference in absolute, and relative, populations)

---
Te Dependency

---
ne Dependency

---
N0 Dependency

---
Texas Helimak
ECRH: 6kW @ 2.45GHz
Uniformity in vertical direction.
Variations in radial direction.
Measurement of electron temperature and density via Langmuir probes at top and bottom.
Parameters
[3]

---
External Photo

---
Internal Photo

---
Measurement Method
One radial position per shot.
Calibration for view-port, lens, fiber, and spectrometer.
Assume uniformity of plasma

---
Argon Plasma Spectrum

---
Measured Lines
Upper Level
Model
Upper Level
Model
800.616
696.54
9
7
706.72
8
801.479
7
810.369
714.70
8
7
811.531
727.29
9
7
826.452
738.398
8
9
840.821
8
750.387
11
842.465
7
751.465
10
852.144
763.51
7
8
772.376
7
866.79
7
772.421
9
912.3
6
794.818
8
922.45
7
overlap

---
Measured Lines (cont.)
Upper Level
Model
935.42
7
965.78
6
978.45
7

---
Measure and Fit to Level Density
Intensity proportional to level density.
Average values from all independent lines.
Neutral density as free parameter: Te, ne fixed at each position.

---
Temperature & Density Est.
(at radial positions where spectra were taken)
Electron Temperature
R (m)
Te (eV)
Electron Density
R (m)
ne (cm-3)

---
Level Densities

---
Comparison of Lines
Radial position R = 0.96m
Coeff. Of Det.

---
Measured Versus Best Fit

---
Comparison of Lines (cont.)
Radial position R = 1.27m
Coeff. Of Det.

---
Neutral Density Best Fit
Fill Pressure:

---
Fitting to Measure ne and Te
Absolute level densities depend on n0, ne, and Te nearly linearly.
Must depend on relative intensities to remove ambiguities.
  - Only 6 independent levels for all measured lines.
  - Choose lines to represent levels.

---
Est. Level Population Ratios
~10% or less variation

---
Testing Level Groupings
Level 7 and 8 in model consists of several non-degenerate physical levels.
Line intensities determined by statistical weight:
All lines should predict the same level density.
Line ratios should be fixed, and not depend on plasma parameters.

---
Level 7 Line Ratios
3.1
0.58
0.2

---
Level 7 Line Ratios (cont)
Radial Position R=0.96m

---
Level 8 Line Ratios
2.94
2.19
2.23
0.01

---
Conclusions
Levels up to level 25 in model are important to predict absolute and relative intensities.
Produces good fit to measured intensities with some deviations. ( )
Fitted values show variations of neutral density.
Fitting to determine electron density or temperature more difficult from the measured lines.
Grouping of some levels may not be justified.

---
References
I.I. Sobelman, L.A. Vainshtein, and E.A. Yukov, Excitation of Atoms and Broadening of Spectral Lines (Springer-Verlag Berlin Heidelberg New York 1981)
A. Bogaerts et al, Journal of Applied Physics Vol. 84, No. 1, 121 (1998)
K. Gentle, Huang He, Texas Helimak, Plasma Science and Technology, Vol.10, No. 3 (Jun. 2008)
H. R. Griem, Principles of Plasma Spectroscopy (Cambridge University Press 1997)
E. M Sciamma, Plasma Spectroscopic Diagnostic Tool Using Collisional-Radiative Models and its Application to Different Plasma Discharges For Electron Temperature and Neutral Density Determination, U. Texas Austin Dissertation (2007)